## Slide 1
Internet of Things (IoT)

## Slide 2: Outline
Introduction to IoT
Enabling technologies
Open problems and future challenges
Applica1ons
2

## Slide 3: What is IoT?
A phenomenon which connects a variety of things
– Everything that has the ability to communicate
3

## Slide 8: IoT Deﬁni1ons
The Internet of Things, also called The Internet of Objects, refers to a wireless network between objects, usually the network will be wireless and self‐conﬁguring, such as household appliances. (Wikipedia)
The term "Internet of Things" has come to describe a number of technologies and research disciplines that enable the Internet to reach out into the real world of physical objects. (IoT 2008)
“Things having iden11es and virtual personali1es opera1ng in smart spaces using intelligent interfaces to connect and communicate within social, environmental, and user contexts”. (IoT in 2020)
5

## Slide 9: Characteris1cs of IoT
Intelligence
  Knowledge extrac1on from the generated data
Architecture
  A hybrid architecture suppor1ng many others
Complex system
  A diverse set of dynamically changing objects
Size considera1ons
  Scalability
Time considera1ons
  Billions of parallel and simultaneous events
Space considera1ons
  Localiza1on
Everything‐as‐a‐service
  Consuming resources as a service
8

## Slide 10: IoT Layered Architecture
9
Sensing And Communica>on
Middleware and Applica>ons
Source: ZTE

## Slide 11: Networking and Communica1on
RFID to smallest enabling technologies, such as chips, etc.
10
Source: Qian Zhang. Lecture notes. 2013

## Slide 12: RFIDs
The reduc1on in terms of size, weight, energy consump1on, and cost of the radio takes us to a new era
– This allows us to integrate radios in almost all objects and thus, to add the world ‘‘anything” to the above vision which leads to the IoT concept
Composed of one or more readers and tags
RFID tag is a small microchip a`ached to an antenna
Can be seen as one of the main, smallest
components of IoT, that collects data
11

## Slide 13: Wireless Technologies
Telecommunica1on systems
  Ini1al/primary service: mobile voice telephony
  Large coverage per access point (100s of meters – 10s of kilometers)
  Low/moderate data rate (10s of kbit/s – 10s of Mbits/s)
  Examples: GSM, UMTS, LTE(4G/5G Long term Evaluation)
WLAN
  Ini1al service: Wireless Ethernet extension
  Moderate coverage per access point (10s – 100s meters)
  Moderate/high data rate (Mbits/s – 100s)
  Examples: IEEE 802.11(a‐g), Wimax
12
Source: Geert Heijenk. Mobile and Wireless Networking. Lecture Notes. 2014

## Slide 14: Wireless Technologies
Short range:
  Direct connec1on between devices – sensor networks
  Typical low power usage
  Examples: Bluetooth, Zigbee, Z‐wave (house products)
Other examples:
  Satellite systems
    Global coverage
    Applica1ons: audio/TV broadcast, posi1oning, personal communica1ons
  Broadcast systems
    Satellite/terrestrial
    Support for high speed mobiles
  Fixed wireless access
    Several technologies including DECT, WLAN, IEEE802.16, etc.
13
Source: Geert Heijenk. Mobile and Wireless Networking. Lecture Notes. 2014

## Slide 15: Sensor Networks (SNs)
Consist of a certain number (which can be very high) of sensing nodes (generally wireless) communica1ng in a wireless mul1‐hop fashion
14
Source: Perera et al. 2014

## Slide 16: Sensor Networks (SNs)
SNs generally exist without IoT but IoT cannot exist without SNs
SNs have been designed, developed, and used for speciﬁc applica1on purposes
  Environmental monitoring, agriculture, medical care, event detec1on etc.
For IoT purposes, SNs need to have a middleware addressing these issues:
  Abstrac1on support, data fusion, resource constraints, dynamic topology, applica1on knowledge, programming paradigm, adaptability, scalability, security, and QoS support
15

## Slide 17: Networked Infomechanical Systems (NIMS)
Networked mobile nodes
  Sensing
  Sampling
  Energy logistics
  Communication
Infrastructure
  Deterministic and precise motion
  3-D volume access
  Mass transport at low energy
System Ecology for Sustainability
  Fixed nodes
  Mobile nodes
  Infrastructure

## Slide 18: Habitat Monitoring on Great Duck Island
http://www.greatduckisland.net/
Intel Research Laboratory at Berkeley initiated a collaboration with the College of the Atlantic in Bar Harbor and the University of California at Berkeley to deploy wireless sensor networks on Great Duck Island, Maine (in 2002)
Monitor the microclimates in and around nesting burrows used by the Leach's Storm Petrel
Goal : habitat monitoring kit for researchers worldwide

## Slide 19: Sensor Nodes
Worldsens Inc. Sensor Node
Crossbow Sensor Node

## Slide 20: Sensor Node Components

## Slide 21: WSN Communication Architecture

## Slide 22: Different Targets
mica | mica2 | mica2dot | micaz
telos | telosb | rene2 | pc

## Slide 23: Mica2 Clone

## Slide 24: TELOSB MOTE
Ref:http://www.eecs.berkeley.edu/~culler/eecs194/labs/lab1/telosb.JPG

## Slide 25: One Example Sensor Board - MTS310

## Slide 26: WSN Simulators
NS-2
GloMoSim
OPNET
SensorSim
J-Sim
OMNeT++
Sidh
SENS

## Slide 27: WSN Emulators
TOSSIM
ATEMU
Avrora
EmStar

## Slide 28: Example: Indoor Localiza1on
An indoor positioning system (IPS) is a solution to locate objects or people inside a building using radio waves, magnetic fields, acoustic signals, or other sensory information collected by mobile devices.
For indoor localization:
  Any wireless technology can be used for locating
  GPS, WiFi, Bluetooth, RFID, Ultrawide band, Infrared, Visible light communication, Ultrasound
16

## Slide 29: Middleware
Middleware is a so/ware layer that stands between the networked opera4ng system and the applica4on and provides well known reusable solu4ons to frequently encountered problems like heterogeneity, interoperability, security, dependability [Issarny, 2008]
IoT requires stable and scalable middleware solu1ons to process the data coming from the networking layers
17

## Slide 30: Service Oriented Architecture (SOA)
18
Middleware solu1ons for IoT usually follow SOA approaches
Allows SW/HW reuse
  Doesn’t impose speciﬁc technology
A layered system model addressing previous issues
  Abstrac1on, common
services, composi1on
Source: Atzori et al. 2010

## Slide 31: Other Middleware Examples
Fosstrak Project
  Data dissemina1on/aggrega1on/ﬁltering/interpreta1on
  Fault and conﬁgura1on management, lookup and directory service, tag ID management, privacy
Welbourne et al.
  Tag an object/create‐edit loca1on info/combine events collected by antennas
e‐Sense Project
  Middleware only collects data in a distributed fashion and transmits to actuators
UbiSec&Sens Project
  Focuses on security  secure data collec1on, data store in
memory, etc.
19

## Slide 32: Open Problems and Challenges
Lack of standardiza1on
Scalability
  Addressing issues
  Understanding the big data
Support for mobility
Address acquisi1on
New network traﬃc pa`erns to handle
Security/Privacy issues
20

## Slide 33: Standardiza1on
Several standardiza1on eﬀorts but not integrated in a comprehensive framework
Open Interconnect Consor1um: Atmell, Dell, Intel, Samsung and Wind River
Industrial Internet Consor1um: Intel, Cisco, GE, IBM
AllSeen Alliance: Led by Qualcomm, many others
21

## Slide 34: Scalability
Number of devices increasing exponen1ally
  How can they uniquely be tagged/named?
  How can the data generated by these devices be managed?
22

## Slide 35: Addressing Issues
Incredibly high number of nodes, each of which will produce content that should be retrievable by any authorized user
  This requires eﬀec1ve addressing policies
  IPv4 protocol may already reached its limit. Alterna1ves?
  IPv6 addressing has been proposed for low‐power wireless communica1on nodes within the 6LoWPAN context
IPv6 addresses are expressed by means of 128 bits 1038 addresses, enough to iden1fy objects worth to be addressed
RFID tags use 64–96 bit iden1ﬁers, as standardized by EPCglobal, solu1ons to enable the addressing of RFID tags into IPv6 networks
Encapsulation of RFID message into an IPv6 packet.
23

## Slide 36: New Traﬃc to Handle
The characteris1cs of the smart objects traﬃc in the IoT is s1ll not known
  Important  basis for the design of the network infrastructures and protocols
Wireless sensor networks (WSNs) traﬃc characteriza1on
  Strongly depend on the applica1on scenario
  Problems arise when WSNs become part of the overall Internet
  The Internet will be traversed by a large amount of data generated by sensor networks deployed for heterogeneous purposes  extremely diﬀerent traﬃc characteris1cs
  Required to devise good solu1ons for suppor1ng quality of service
24

## Slide 37: Security
25
Man in the middle attack Source: Atzori et al. (2010)
The components spend most of the 1me una`ended
  It is easy to physically a`ack them
IoT components are characterized by low capabili1es in terms of both energy and compu1ng resources
  They can’t implement complex schemes suppor1ng security
Authen1ca1on problem
  Proxy a`ack, a.k.a. man in the middle a`ack problem
    Data integrity
      Data should not be modiﬁed without the system detec1ng it
      A`acks on the node
        Memory protec1on
      A`acks over the network
        Keyed‐Hash Message Auth. Code

## Slide 38: Privacy
How is it diﬀerent than tradi1onal privacy?
  Legisla1ve issues
  Ethics issues
Easy for a person to get involved in IoT even if he/she does not know
Data can be stored indeﬁnitely
Current solu1ons are not enough
  Encryp1on, pseudo‐noise signal, privacy broker
26

## Slide 39: Again ‐ Overall Picture
27
Source: “What the Internet of Things (IoT) Needs to Become a Reality,” White Paper, by K. Karimi and G. Atkinson

## Slide 40: Applica1ons
Several diﬀerent domains
  Transporta1on and logis1cs
  Healthcare
  Smart environment (home, oﬃce, etc.)
  Personal and social domain
28

## Slide 41: Applica1on Domains and Scenarios
29

## Slide 42: Healthcare Applica1ons
Various sensors for various condi1ons
Example ICP sensor: Short or long term monitoring of pressure in the brain cavity
Implanted in the brain cavity and senses the increase of pressure
Sensor and associated electronics encapsulated in safe and biodegradable material
External RF reader powers the unit and receives the signal
Stability over 30 days so far 30

## Slide 43: Healthcare Applica1ons
Other applica1ons:
  Na1onal Health Informa1on Network
  Electronic Pa1ent Record
  Home monitoring and control
    Pulse oximeters, blood glucose monitors, infusion pumps, accelerometers
  Bioinforma1cs
    Gene/protein expression
    Systems biology
    Disease dynamics
31

## Slide 44: Environmental Applica1on: Ci1Sense
Air quality monitoring project in UCSD CSE
Environmental applica1on
Electrochemical sensors, microcontroller for data collec1on and transmission to an Android app
Actua>on: air quality is immediately reported, as well as retransmi`ed to a backend for larger‐scale analysis
32

## Slide 45: Transporta1on Applica1ons
Vehicle control: Airplanes, automobiles, autonomous vehicles
  All kinds of sensors to provide accurate, redundant view of the world
  Several processors in cars (Engine control, break system, airbag deployment system, windshield wiper, door locks, entertainment system, etc.)
  Actua1on is maintaining control of the vehicle
  Very 1ght 1ming constraints and requirements enforced by the plarorms
33

## Slide 46: Example Transporta1on Scenarios
A network of sensors in a vehicle can interact with its surroundings to provide informa1on
  Local roads, weather and traﬃc condi1ons to the car driver
  Adap1ve drive systems to respond accordingly
Automa1c ac1va1on of braking systems or speed control via fuel management systems.
  Condi1on and event detec1on sensors can ac1vate systems to maintain driver and passenger comfort and safety through the use of airbags and seatbelt pre‐tensioning
Sensors for fa1gue and mood monitoring based on driving condi1ons, driver behavior and facial indicators
  Ensuring safe driving by ac1va1ng warning systems or directly controlling the vehicle
34

## Slide 47: Smart Home Applications
Smart meters, hea1ng/cooling, mo1on/temperature/ ligh1ng sensors, smart appliances, security, etc.
35

## Slide 48: A Futuristic Applica1on: Shopping
When entering the doors, scanners will iden1fy the tags on her clothing.
When shopping in the market, the goods will introduce themselves.
When paying for the goods, the microchip of the credit card will communicate with checkout reader.
When moving the goods, the reader will tell the staﬀ to put a new one.
36